## Slide 1: Characterizing the Annual Surface Energy Balance in Gothic Valley during the SPLASH Field Campaign
Brian Butterworth1,2, Christopher Cox2, Gijs de Boer1,2, Michael Gallagher1,2,
Janet Intrieri2, Ola Persson1,2, Matthew Shupe1,2
1 Cooperative Institute for Research in Environmental Sciences (CIRES), CU Boulder
2 NOAA Physical Sciences Laboratory

## Slide 2: Atmospheric Surface Flux Stations
Here we investigate changes in the surface energy balance that were observed as wintertime snowpack transitioned
to the snow-free
summer environment.
high freq UVW, H2O, & T
soil flux plates (5 cm)
soil T & VWC (0 - 50 cm)
Near surface T, P, RH, U
System ran continuously
3
Kettle Ponds Avery

## Slide 3: Energy Balance Equation
RN = Net Radiation
G = Ground Flux
HL = Latent Heat Flux
HS = Sensible Heat Flux
S = Storage
The Problem:
Energy Balance Non-Closure
It is typical for traditional EC to measure greater incoming energy (net radiation - ground flux) than outgoing energy (sensible + latent heat flux); even though they are expected to balance.
3

## Slide 4
As is typical for EC measurements, we observed energy fluxes that were lower in magnitude than the available energy (RN – G), resulting in an energy balance residual (Imb)
A seasonal cycle in Imb was observed – with negative daily mean values in winter and large positive values in summer
Daily mean Imb magnitudes were often larger than each of HS, HL, and G.
4

## Slide 5: Snow Melt Period (Avery)
Imbalance increases as snow melt begins
Snow melts over 1 month period
Period coincides with ground water melt
What portion of imbalance is from snow/ground melt energy?
5

## Slide 6: Snow Melt Energy Flux
= mass of water = depth of melt * snow density
= heat of fusion = 334 J / g H2O
6

## Slide 7: Snow Melt Energy Flux
Depth of melt =1.2 m
Snow density ~ 0.25
= 1.2 m * 1 m2 *0.25 = 0.3 m3
45 W m-2
26 days
1.2 m
7

## Slide 8: Snow Melt Energy Flux
Avery
48 W m-2
Kettle Ponds
47 W m-2
8

## Slide 9: SNOTEL
Snow Density = SWE / Snow Depth
Mean snow density was ~25%
Snow density changed throughout season
*Adjustments to
melt flux required
9

## Slide 10: Ground Melt Energy Flux
= depth of layer * volumetric water content
10

## Slide 11: Imbalance minus Melt Energy
Accounting for melt balances the energy budget during snow melt period
Caveats
Doesn’t account for:
Sublimation
Refreezing
11

## Slide 12: Next Steps
Improve snow density estimate
Determine frozen soil water content
Remove sublimation contribution from melt flux
Identify cause of missing energy during the rest of summer
(Photo credit: Heidi Steltzer)

## Slide 14: Avery Kettle Ponds
4

## Slide 15
Diurnal Imb values were largest during the daytime
Imb magnitudes were roughly 40% of RN magnitudes. This is particularly large and may be due to the omission of advection, flux divergence, and/or topographic effects